## Slide 1: ToolChain
IOTivity-Lite Code explained

## Slide 2: The Generated IOTivity-Lite code explained
IOTivity-Lite API
Main
Supported functions
Global variables for each resource
Handler implementation for each resource-method

## Slide 3: Typical stages, setup and running of the stack
initialize
stack
build in resources
Run (wait on callback)
GET: create response
POST:
application specific resources
Process (assign) input
Check input
Create response

## Slide 4: IOTivity-lite build in resources
Set of APIs to create an OCF device (or client)
Has a set of “build-in” resources:
  oic/res
  oic/p
  oic/d
  Security resources
  introspection
The entity handler of these resources will be handled by the stack.

## Slide 5: Main
Main
  Starts the platform
  Register the device and platform, e.g. initializes oic/d and oic/p
  Create all application specific resources
  Message pump
    A loop that handles the incoming messages, e.g. GET and POST
      Calls the installed callbacks for each resource.
    This loop makes sure that all access to the functions/global variables are not concurrent.

## Slide 6: Register device (app_init)
app_init function sets the device (oic/d) information like:
Device type
Device name
Data model versions
No specific things that is being set the platform
- Only name

## Slide 7: Register resources
register_resources function sets for each endpoint:
Resource type
Interface, including the default interface
Discoverable
Observable
And the GET/POST request handlers

## Slide 8: Resource global variables
Each end point has a set of variables:
The property name
  naming convention: g_<path>_RESOURCE_PROPERTY_NAME_<propertyname>
The actual value of the property, which is typed from the json data type
  naming convention: g_<path>_<propertyname>
The path in a variable:
  naming convention: g_<path>_RESOURCE_ENDPOINT
Array of interfaces, where by the first will be set as default interface
  naming convention g_<path>_RESOURCE_INTERFACE

## Slide 9: Handling the Retrieve (GET) operation
Each endpoint can have an Retrieve (GET) operation:
Naming convention: get_<path>
Function returns the payload when “coap-get” is called
Function adds the global variables of that specific endpoint to the payload that will be returned
Implementation specific:
before assigning the member variables to the payload, one can update the member variables from the HW.

## Slide 10: Handling the Update (POST) operation
Each endpoint can have an UPDATE function:
Naming convention: post_<path>
Function that interprets the payload when “coap-post” is called
Function checks if the properties are correct and within the limits.
If all properties are correct, then the values of the post are assigned to the global variables for that specific endpoint
Implementation specific:
after assigning the value to the member variables, one can interact with the HW, using the newly assigned member variables.