## Slide 1: OCF 2.0.1 Security Primer for Device Vendors
Q1 2019
Nathan Heldt-Sheller

## Slide 2: The Primary Roles of the OCF Security Layer
From a "normal" (non-security-expert) developer's perspective, the OCF Security Layer has two primary functions:
Device Onboarding – "pairing" a New Device (e.g. Out of Box) to the owner's domain. An example would be connecting a newly-installed lightbulb (a Server Device) to the home's OCF lighting control (a Client Device application).
Access Control – filtering incoming requests to a Device, and making a "Granted" or "Denied" decision for each request before it is passed to the Resource endpoint.
  Note: for the security-minded, this includes authentication in addition to authorization.
Both of these functions are achieved via a set of "Security Virtual Resources" (SVRs), which provide the interface through which Device Onboarding is accomplished, and Access Control is configured.

## Slide 3: Onboarding a New Device (Lightbulb) Using an App (OBT) on Mom's Phone
  Mom screws in the new lightbulb
  Mom opens the OCF App on her Phone
  Mom clicks the "refresh" icon and finds the lightbulb
  Mom clicks the "+" button and onboards the lightbulb to the Smith Home network
    Behind the scenes, the OBT performs the Certificate-based OTM
    When finished, Mom's App is now able to control the lightbulb
  Mom is prompted "Should 'Family' group members to be able to control this lightbulb?"
  Mom clicks "yes"
    Other Clients that are part of the Family group can now control the lightbulb as well
Mom's App
Find New Devices
New Lightbulb
Mom's Lightbulb
Should 'Family' group members be able to control this lightbulb?
Yes
No
Family Lightbulb

## Slide 4: Dad's Phone is added to the Smith Home domain
  Dad installs and opens OCF App, but is not yet joined to the Smith Home domain
  Mom opens the OCF App on her Phone
  Mom clicks the "refresh" icon and finds Dad's phone. Mom's phone prompts her to onboard Dad's phone
    Mom clicks "yes" and Dad's phone is onboarded, but still doesn't have access to the lightbulb
  Mom's phone prompts her to add Dad to the Family Group
    Mom clicks "yes" and Dad can now control the Lightbulb
Mom's App
Find New Devices
Family Lightbulb
Dad's App
Would you like to join Dad's Phone to the Smith Home network?
Yes
No
Would you like to add Dad's App to the Family Group?
Yes
No
Find New Devices
Family Lightbulb

## Slide 5: How This All Works in OCF: Introducing the Security Virtual Resources (SVRs)
Although there are quite a few SVRs defined in the OCF Security Specification, there are just four that are essential to understanding basic security function:
/oic/sec/doxm (or "/doxm") – The Device Owner Transfer (Xfer) Method Resource
  The /doxm Resource provides the interface for taking ownership of a Device. Usually, taking ownership is the first step in onboarding a new Device into the owner's domain.
/oic/sec/pstat (or "/pstat") – The Provisioning Status Resource
  The /pstat Resource is used to manage further provisioning of a Device, after ownership is established. Specifically, the /pstat Resource is used to put the Device in "Ready for Normal Operation" (RFNOP) state, which signals that the Device is fully configured and ready to start its normal steady-state functioning (e.g. a lightbulb in "RFNOP" is ready to handle "on/off/dim" requests from the Lighting Controller App).
/oic/sec/acl2 (or "/acl2") – the Access Control List Resource
  The /acl2 Resource is used to configure the access control policy on the Device (i.e. which Clients are allowed to access which Resources, and what the access-modes – Retrieve vs. Update, etc – are allowed).
/oic/sec/cred (or "/cred") – The Credentials Resource
  The /cred Resource stores the credentials – cryptographic keys, certificates, etc. – that are required to establish secure connections, and verify Client identity, among other things.

## Slide 6: Understanding /doxm
/oic/sec/doxm (or "/doxm") – The Device Owner Transfer (Xfer) Method Resource
  The /doxm Resource provides the interface for taking ownership of a Device. Usually, taking ownership is the first step in onboarding a new Device into the owner's domain.
  "doxm": {
  "oxms": [0],
  "oxmsel": 0,
  ...
  "deviceuuid": "20202020-2020-2020-2020-202020202020",
  ...
  "rowneruuid": "10101010-1010-1010-1010-101010101010"
  }
"oxms" lists the onboarding modes a Device supports
"oxmsel" selects the chosen onboarding mode
"deviceuuid" is the UUID (Universally Unique Identifier) of the Device
"rowneruuid" is the UUID of the /doxm Resource Owner

## Slide 7: Understanding /pstat
/oic/sec/pstat (or "/pstat") – The Provisioning Status Resource
  The /pstat Resource is used to manage further provisioning of a Device, after ownership is established.
  "pstat": {
  "dos": { "s": 3, "p": false },
  ...
  "rowneruuid": "10101010-1010-1010-1010-101010101010"
  }
"dos" "s" is the Device Onboarding State of the Device.
1 = Ready for Ownership Transfer
2 = Ready for Provisioning
3 = Ready for Normal Operation
"rowneruuid" is the UUID of the /pstat Resource Owner
"dos" "p" is true IFF a change to "s" is pending. When true, new Update requests to "s" will be rejected.

## Slide 8: Understanding /acl2
/oic/sec/acl2 (or "/acl2") – the Access Control List Resource
  The /acl2 Resource is used to configure the access control policy on the Device (i.e. which Clients are allowed to access which Resources, and what the allowed access-modes – Retreive vs. Update, etc – are allowed.
  "acl": {
  "aclist2": [
  {
  "aceid": 1,
  "subject": { "conntype": "anon-clear" },
  "resources":
  [{ "href": "/a/light" }],
  "permission": 2
  },
  ...
  ],
  "rowneruuid" : "10101010-1010-1010-1010-101010101010"
  }
"aclist2" is an array of Access Control Entries (ACEs) which lists all the Requests that will be Granted.
NOTE: Any request NOT Granted by an ACE is by default Denied
"aceid" is an identifier that can be used to manage the ACE
"rowneruuid" is the UUID of the /acl2 Resource Owner
"subject" describes the Clients to which this ACE Grants access
"resources" lists the Resources to which this ACE Grants access
"permission" is a bitmask
of request types allowed by this ACE, read in reverse CRUDN (i.e. NDURC). E.G.:
(2 = 0b00010 = ----R-)

## Slide 9: Understanding /cred
/oic/sec/cred (or "/cred") – The Credentials Resource
  The /cred Resource stores the credentials – cryptographic keys, certificates, etc. – that are required to establish secure connections, and verify Client identity, among other things.
"creds" is an array of credentials (key, certificate, etc.) installed on this Device
"credid" is an identifier that can be used to manage the credential
"rowneruuid" is the UUID of the /cred Resource Owner
"subjectuuid" lists the UUID of the Device corresponding to this credential
"credtype" is the type (symmetric key, certificate, etc.) of this credential
"period" determines the timeframe for which this credential is valid
  "cred": {
  "creds": [
  {
  "credid": 2,
  "subjectuuid": "30303030-3030-3030-3030-303030303030",
  "credtype": 1,
  "period": "20150630T060000/20990920T220000",
  "privatedata": {"data": "AAAAAAAAAAAAAAAA", ...}
  },...],
  "rowneruuid": "10101010-1010-1010-1010-101010101010"
  }
"privatedata" contains the strictly-confidential
keying material

## Slide 10: Onboarding Methods (OTMs) at a Glance
JustWorks OTM – the most basic onboarding method for getting Device into RFNOP
+ simple and functional
- vulnerable to MitM attacks on the onboarding network
RFOTM
(start)
RFPRO
RFNOP
(end)
Step 1 - "Ready for OTM" Device Out of Box state
Step 2 - "Ready for Provisioning" Configure /acl2 etc.
Step 3 - "Ready for Normal Operation" Device steady state
Nominal Onboarding Flow
Random PIN OTM – require the User to enter a PIN to complete onboarding
+ resists MitM
- requires User Input (higher touch)
- requires PIN display and Input method to communicate PIN from Server->User->OBT
Certificate OTM – New Device supplies a Certificate to Onboarding Tool
+ best assurance and most informed onboarding decision via Cert meta-data
- requires Certificate capabilities (incl. Root Cert in OBT)
O
T
M

## Slide 11: Onboarding a Device – an Incomplete Illustration
Onboarding Tool (OBT)
UUID 10.*
New Device
UUID 20.*
Discover un-owned Device (multicast GET to /doxm ? owned = false)
Select desired OTM (POST to /doxm.oxmsel = JUST_WORKS)
Response (/doxm Resource)
Take ownership (POST to /doxm, incl. /doxm.rowneruuid = 10.* )
Move to New Device to RFPRO state (POST to /pstat.dos.s = RFPRO )
Provision Access Control (POST to /acl2 with various ACE entries)
Note that in JUST_WORKS OTM, there is a step (not shown) wherein both parties calculate a shared credential, and store it in the /cred Resource
Provision Additional Credentials (POST to /cred)
Move to New Device to RFNOP state (POST to /pstat.dos.s = RFNOP )
Device is now ready to service "Vertical Resource" (e.g. /a/light) requests

## Slide 12: Access Control using Groups and Wildcards
"Access Control" – filtering incoming requests to a Device, and making a "Granted" or "Denied" decision for each request before it is passed to the Resource endpoint.
OCF defines the /acl2 Resource, which contains "Access Control Entry" objects (ACE2), to configure Access Control for a Device.
Within an ACE2, there is a "subject" Property, which determines the Client(s) which may be Granted access by the ACE2, and this is where Group Access comes in
Separate but related in the "resources" Property, which determines the Resource(s) to which the ACE2 applies

## Slide 13: Processing a Request with Access Control applied
Client Device
UUID 30.*
Lightbulb Device
UUID 20.*
Discover Resources
Connect to Secure Endpoint (e.g. CoAPS/DTLS)
Response 2.04 (/res Resource)
Retrieve /a/light
At this point, an Access Control check takes place. The /acl2 Resource is consulted, and the Request is Granted based on (for example) an ACE which grants requests from Device UUID 30.* "Read" access to the /a/light Resource.
To establish a secure connection (e.g. DTLS) the credential associated with this Client's UUID is looked up in the /cred Resource, and used to verify the identity of the Client Device.
Update /a/light
Response 2.04 (/a/light Resource)
Response 4.01 ("Unauthorized")
Again, an Access Control check takes place. The /acl2 Resource is consulted, and the Request is Denied because no ACE grants Client Device with UUID 30.* "Update" access to the /a/light Resource.

## Slide 14: "subject" Groups
Two pre-defined groups, via the "conntype" Parameter of the ACE2 "subject" property:
  "anon-clear" – all Subjects which are connected via anonymous, clear-text channel
  "auth-crypt" – all Subjects which are connected via authenticated, encrypted channel
  {
  "aceid": 1,
  "subject": { "conntype": "anon-clear" },
  ...
  }
Vendor-defined groups, via "roletype" Parameter of the ACE2 "subject" property:
  Symmetric keys: (1) "role" per Client, keyed on UUID
  Certificates: n "roles" per Client, keyed on public key
  {
  "aceid": 1,
  "subject": { "roletype": "<made_up_string_that_matches_string_in_cred>" },
  ...
  }

## Slide 15: "resources" Wildcards
Beginning in OCF 2.0, we have reduced the scope of these wildcards
  "*" – all Non-Configuration Resources
    NCRs exclude discovery and configuration Resources; see Security Specification Terms and Definitions
  "+" – all NCRs exposing a Secure Endpoint
  "-" – all NCRs exposing an Unsecure Endpoint
  With these new definitions, a basic /acl2 configuration where "auth-crypt" has access to "+" and "anon-clear" has access to "-" may be a suitable baseline access control configuration for many Devices. It essentially means that any Client which has been onboarded can access all the Non-Configuration Resources on that Server.

## Slide 16: Symmetric Keys vs. Certs – Credential management and Access Control management implications
There are security and performance related considerations for both, which should be understood by a Device Vendor choosing its credential model. OCF's access control model has additional implications that should be taken into account.
Implication to Credential (/cred Resource) Management: using Symmetric Keys requires higher-touch key management.
  In short, each time a New Client is added to the domain, the symmetric credential model requires each Server Device in the domain to be provisioned with a new symmetric credential, before the Dad's App can establish an authenticated connection with that Server.
  By contrast, the certificate model allows the Server Device to mutually authenticate with Dad's App using the Root Cert (or CA Cert) already installed on the Server; the Server isn't touched when Dad's App is added.
Implications to Access Control (/acl2 Resource) Management: using Certs enables more granular group-level access.
  With a symmetric credential installed on the Server, the New Client will match all "conntype":"auth-crypt" ACEs, and thus gain that level of access permission
    Furthermore, a Client-specific ACE – naming the New Client by its UUID – can be installed to give the Client additional access permission
  In a certificate model, the New Client will also match all "auth-crypt" ACEs, but can also be granted access to any "role" ACEs, on a per-role basis
    The OBT just needs to the New Client a "role certificate" which is then supplied to the Server during connection establishment, and authorizes the New Client to effectively join the security group named in the "role"

## Slide 17: Security Profiles (/sp) at a Glance
"Baseline" sets the minimum requirement for every OCF Device
On top of "Baseline", each Security Profile defines an optional set of additional security features and requirements
If a Device Vendor chooses to meet these requirements, and the Device can be certified by OCF as such, the /sp Resource can tell an Onboarding Tool/Client which Profiles the Device supports. This can aid the Client in determining how trustworthy a given Device is.
Baseline Profile
  The minimum security requirements for every OCF Device
Black Profile
  Requires use of the OCF PKI
  Additional improved robustness requirements above Baseline Profile
Blue Profile
  Requires auditing of the Manufacturer CA
  Additional improved robustness requirements above Baseline Profile
Purple Profile
  Requires a handful of specific security features
  Requires auditing of the Manufacturer CA
  Additional improved robustness requirements above Baseline Profile
The OCF 2.0.1 Profiles