## Slide 1: ToolChain
Code generation

## Slide 2: Code generation
Code generation is possible due to :
All Resources are defined in an machine readable format
  Using OpenAPI 2.0 definitions
  Defines resource by:
    Which operations are supported (RETRIEVE, UPDATE, ..)
    Schema definition of the payload per operation
    An example of the payload
    Define which query parameters are applicable

## Slide 3: The DeviceBuilder tool chain

## Slide 4: The DeviceBuilder toolchain
The DeviceBuilder tool chain consist of a set of python scripts glued together with bash scripts.
The script installs the necessary depended info it needs:
  Git repos
  Install python3 packages using pip3
The chain works on Linux and on Window (using git bash).
The chain will be used on a raspberry pi

## Slide 5: DeviceBuilder
Python script to merge the resources to be used into a single file.
Takes an set of resources that will be used in the implementation
  Combines swagger resource files into 1 large swagger file
    Renames paths and removes properties while processing.
  Does this for optional core resources and all resources in oneIOTa.
    Mandatory resources (core and security) are not processed.
Input: file with resources to be implemented
Output: swagger file that list all “application level” resources
  All resources that the application needs to implement to function correctly.

## Slide 6: swagger2x
Create code by means of template technology
  Can used jinja2 template technology because OpenAPI 2.0 == JSON
  Add a bit of glue so that JSON constructs can be converted into correct code
  Jinja2 constructs allows to loop over the DOM of the swagger file
    Convert by means of instructions in template all the info of the swagger file into code
    The “clever bit” is in the template, it is an mix of the target code and template language
    An template is targeted for an specific code base
      Multiple templates can co-exist, hence the tool can support all languages/APIs
      Target: C IOTivity-Lite API.
Input: generated swagger file from DeviceBuilder
Output: C code!

## Slide 7: Introspection generation
json2cbor
Tool to convert json to cbor (and visa versa)
Used as first step to create cbor of the introspection file
cbor2include
Utility to create include files from cbor
Only used to convert the cbor introspection file into an include file
Note:
Include file is updated when code generation is done.
  Hence it will always reflect the implementation
  It will be updated in the tree, hence each build will have an updated introspection device data.

## Slide 8: Single script
Single bash script uses the python scripts to create code
Input:
Input file with the wanted resources
Output directory
Which device type is being implemented
For example:
sh DeviceBuilder_IotivityLiteServer.sh ../input-lightdevice.json ../lightdevice "oic.d.light"

## Slide 9: What do you get?
After running the DeviceBuilder script:
Output Directory with:
  Code currently based on C API of IOTivity-Lite 1.3.1
  Introspection file that matches the implementation
    Available in JSON and CBOR (converted from JSON)
  Initial just works security file
    Just a copy of an existing file
Problem: how to build this code

## Slide 10: Build environment: IOTivity-Lite-setup
Github repo that uses IOTivity-Lite v1.3-rel as build environment and sets up the device builder tool chain to build an application
This github repo sets up an “work area”
  Installs tools/code/etc to build an IOTivity-Lite server application
    Linux
    raspberry pi
  This includes installing a copy of the IOTivity-Lite code
  Github to install the environment resides at:
  https://github.com/openconnectivity/IOTivity-Lite-setup

## Slide 11: IOTivity-Lite-setup github repo
The repo has setup scripts for:
Setting up IOTivity-Lite with code and build environment
  IOTivity version: 1.3-rel
  Sets it up in local folder
Setting up DeviceBuilder
  Relative to IOTivity-Lite folder
Setting up MRAA to interact with the hardware
Everything is set up by executing:
curl https://openconnectivity.github.io/IOTivity-Lite-setup/install.sh | bash

## Slide 12: Folder structure
All folders are placed in the top folder
In this case ~/iot-lite

## Slide 13: Preconfigured commands (in iot-lite folder)
Generate code with gen.sh
Compile code with build.sh
Edit code with edit_code.sh (using nano, editing in the iotivity-lite tree)
Run code with run.sh
Reset to onboarding state with reset.sh
  Using just works, script removes files from the iotivity-lite tree.
The scripts that are convenience wrappers around command line tools.
All paths, etc. are filled in.
Code is generated from example.json.
Code is generated in iotivity-lite/apps

## Slide 14: Example input file: binary switch
[ {
"path" : "/binaryswitch",
"rt" : [ "oic.r.switch.binary" ],
"if" : ["oic.if.a", "oic.if.baseline" ],
"remove_properties" : [ "range", "step" , "id", "precision" ]
}, {
"path" : "/oic/p",
"rt" : [ "oic.wk.p" ],
"if" : ["oic.if.baseline", "oic.if.r" ],
"remove_properties" : [ "n", "range", "value", "step", "precision", "vid" ]
} ]
Path to be used
Which interfaces are supported
rt as look up value
Which properties you do not want
Needed for introspection